## Slide 1: A Short Technical History of Wind Driven Mill in the southern Swedish Province of Skåne
By Brian Horsfield
September 7, 2017

## Slide 2: Grinding Grain
For 1000s of year
Simple hand tools

## Slide 3: Beyond hand power
Animal,
Water,
Wind

## Slide 4: Skåne, southern province of Sweden
Notes: Rich in agriculture, produced grain for several thousand years

## Slide 5: No water power

## Slide 6: Lots of wind
Notes: 10 m/s is 22 miles per hour

## Slide 7: Postmill stubbamölla
Introduced to Skåne in the 1200s
Very common in the 1600s

## Slide 8: Parts of a post mill
Entire mill is mounted on a post or (stubbe)
Wings are turned into the wind by rotating the mill with the tail
Grain sacks were carried up the tail
Flour sacks were carried down the tail

## Slide 9: Running a post mill
Power: wind velocity, sail area, angle to the wind
  Grinding stone rpm: too fast – “burned flour”
Product quality: stone gap, feed rate
Notes: The miller spent most of his time monitoring the product.

## Slide 10: Post mill limitation
More production means more power
  Requires bigger diameter wings
  Which means higher axel
  Which means bigger and heavier house
    therefore harder to turn
Limited to one set of grinding stones
  Customers for both flour and animal feed

## Slide 11: Solution – Holländaren

## Slide 12
Only the top (hatten) rotates
The axle is higher so larger wings
Power 2 or more sets of grinding stones
More space to store grain sacks

## Slide 13: First holländare were small

## Slide 14
Next
Taller
But the wings came close to the ground
And grain sacks need to to be carried in by hand

## Slide 16: Elevator (hiss)

## Slide 19: Steel was expensive

## Slide 20: But became cheaper

## Slide 21: Decline
Low cost electricity
Higher labor costs
  Some mills were simply abandoned

## Slide 22: Decline
Some mills let the wings “drop off” and just ran on electricity

## Slide 23: Decline (cont’d)
Some have been tuned into storage sheds

## Slide 24: Decline (cont’d)
Some have been converted to houses (bostadar, fritidhus)

## Slide 25: Survivors
At the end of the 1800s there were about 1000 möllor in Skåne
Today there are less than 100 of which about 20 function (kan måla)
Övraby stopped in 1975 but is in good condition (gott skick)

## Slide 26: Movie